## Slide 1: The European Spallation Source neutrino Super Beam Marcos Dracos IPHC-Strasbourg

## Slide 2: European Spallation Source as Neutrino Facility for CP violation observation (2nd Oscillation maximum)
νμ→νe

## Slide 3: Oscillation probability (neutrino beams)
"solar"
"atmospheric"
"interference"
matter effect
δCP dependence,
sizable matter effect for long baselines
for antimatter: δCP →-δCP and a→-a
fake matter/antimatter asymetry due to matter effect
Matter-antimatter asymmetry

## Slide 4: δCP and Matter-antimatter asymmetry magnitude
(Jarlskog invariant)
Theoretical models predict that if |sinδCP|≳0.7 (45°<δCP<135° or 225°<δCP<315°), this could be enough to explain the observed asymmetry.
(from the already observed CP violation in the hadronic sector)
(Nucl.Phys.B774:1-52,2007, arXiv:hep-ph/0611338)

## Slide 5: Use all the ESS linac power to go to the second oscillation maximum
but why?

## Slide 6: Neutrino Oscillations with "large" θ13
solar
more sensitivity at 2nd oscillation max.
P(νμ→νe)
L/E
1st oscillation maximum
2nd oscillation maximum
θ13=1º
("small" θ13)
θ13=8.8º
("large" θ13)
dCP=-90
dCP=0
dCP=+90
L/E
for small θ13 1st oscillation maximum is better
for "large" θ13 1st oscillation maximum is dominated by atmospheric term
CP interference
CP interference
solar
atmospheric
atmospheric
θ13=1º
θ13=8.8º
(arXiv:1110.4583)
L/E
L/E
solar
1st oscillation max.: A=0.3sinδCP
2nd oscillation max.: A=0.75sinδCP
(see arXiv:1310.5992 and arXiv:0710.0554)

## Slide 7: Having access to a powerful proton beam…
What can we do with:
5 MW power
2 GeV energy
14 Hz repetition rate
1015 protons/pulse
>2.7x1023 protons/year
p
π
ν
decay tunnel
proton beam
target
hadrons
hadronic collector
(focusing)
Detector
physics
⨂B
conventional neutrino (super) beam

## Slide 8: ESSνSB ν energy distribution
at 100 km from the target, per year (in absence of oscillations)
neutrinos
anti-neutrinos
almost pure νμ beam
small νe contamination which could be used to measure νe cross-sections in a near detector
(Nucl. Phys. B 885 (2014) 127)

## Slide 9: Can we go to the 2nd oscillation maximum using our proton beam?
Yes, if we place our far detector at around 500 km from the neutrino source.
MEMPHYS like Cherenkov detector
(MEgaton Mass PHYSics studied by LAGUNA)
Neutrino Oscillations
Proton decay
Astroparticles
Understand the gravitational collapsing: galactic SN ν
  Supernovae "relics"
Solar Neutrinos
Atmospheric Neutrinos
500 kt fiducial volume (~20xSuperK)
Readout: ~240k 8” PMTs
30% optical coverage
(arXiv: hep-ex/0607026)
New 20" PMTs with higher QE and cheaper (see JUNO), the detection efficiency will improve the detector performance keeping the price constant, not yet taken into account.
see Budimir's presentation

## Slide 10: Neutrinos in the far detector
Below ντ production, almost only QE events, not suffering too much by π0 background.
But, no X-section measurements around 300 MeV ⇒ large systematic error
  need of a performant near detector
540 km (2 GeV), 10 years
neutrinos
anti-neutrinos
2 years
8 years
δCP=0

## Slide 11: 2nd Oscillation max. coverage
2nd oscillation max.
well covered by the ESS neutrino spectrum
1st oscillation max.
νμ→νe

## Slide 12: ESS Linac modifications to produce a neutrino Super Beam
European Spallation Source Linac

## Slide 13: How to add a neutrino facility on top of the neutron one?
The neutron program must not be affected and if possible synergetic modifications.
Linac modifications: double the rate (14 Hz → 28 Hz) and bring the proton energy to 2.5 GeV.
Accumulator (C~400 m) needed to compress to few μs the 2.86 ms proton pulses, affordable by the magnetic horn (350 kA, power consumption, Joule effect) and reducing the atm. neutrino background,
  H- source (instead of protons),
~300 MeV neutrinos.
Target station.
Underground detector.
Short pulses (~μs) will also allow DAR experiments using the neutron target.

## Slide 14: ESSνSB
H- stripping

## Slide 15: Possible locations for far detector
CERN
ESS
Kongsberg
Løkken
LAGUNA sites

## Slide 16: Which baseline?
~60% δCP coverage at 5 σ C.L.
>75% δCP coverage at 3 σ C.L.
systematic errors: 5%/10% (signal/backg.)
CPV (Nucl. Phys. B 885 (2014) 127)
Zinkgruvan
Garpenberg
Candidate active mines

## Slide 17: Candidate active mines
Garpenberg mine
  Distance from ESS Lund 540 km
  Depth 1200 m
  Truck access tunnel
Zinkgruvan mine
  Distance from ESS Lund 360 km
  Depth 1500 m
  Truck access tunnel
Granite drill cores
Lund
Zinkgruvan
(360 km)
Garpenberg
(540 km)
Garpenberg
Zinkgruvan
possible location of MEMPHYS in
Zinkgruvan mine

## Slide 18: Physics Performance
little dependence on mass hierarchy,
δCP coverage at 5 σ C.L. up to 60%,
δCP accuracy down to 6° at 0° and 180° (absence of CPV for these two values),
not yet fully optimized facility,
5/10% systematic errors on signal/background.
540 km
5/5 yrs
see Salvador's presentation

## Slide 19: Do we really need the accumulator
In case the hadron collector current problem is solved, do we still need the accumulator?
  YES, for physics performance reasons

## Slide 20: Required modifications of the ESS accelerator for ESSνSB
Better to go to 2.5 GeV

## Slide 21: The Linac modifications and operation
P
P
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
Into linac
Into ring
Into horn
14 Hz
14 Hz
14 Hz
~1.4 kHz
Horn 1
Horn 2
Horn 4
Horn 3
100 µs
0.65 ms
~1 µs
~0.75 ms
H- source options
see Mamad's presentation

## Slide 22: The Accumulator
4 superperiods
FODO cells
injection
RF
extraction
collimation
Dispersion-free straight sections
Switchyard
H- stripping
lattice development
see Ye's presentation

## Slide 23: General Layout of the target station
Beam Dump
Proton Beam
Collimators
Horns and Targets
Decay Volume
(He, 4x4x25 m3)
8 m concrete
Switchyard
Horns pulse generator
radiation studies
see Eric's presentation

## Slide 24: Target
Helium Flow
other configurations under study

## Slide 25: Muons at the level of the beam dump
muons at the level of the beam dump
(per proton)
y (cm)
x (cm)
4.2x1020 μ/year
(16.3x1020 for 4 m2)
4.1x1020 μ/year
2.7x1023 p.o.t/year
muons/proton
<Eμ>~0.46 GeV
<Lμ>~2.9 km
10-3
input beam for future 6D m cooling experiments (for muon collider),
low energy nuSTORM,
Neutrino Factory,
Muon Collider.
more than 4x1020 μ/year from ESSS compared to 1014 μ used by all experiments up to now (1018 μ for COMET in the future).

## Slide 26: ESS neutrino and muon facility
muon extraction to be studied

## Slide 27: ESSνSB and (R&D) synergies
Super Beam
Neutrino Factory
Muon Collider
+Decay At Rest and Coherent scat.
(with short pulses)
nuSTORM

## Slide 28: EuroNuNet
COST application for networking: CA15139 (2016-2020)
  EuroNuNet : Combining forces for a novel European facility for neutrino-antineutrino symmetry violation discovery (http://www.cost.eu/COST_Actions/ca/CA15139)
  Major goals of EuroNuNet:
    to aggregate the community of neutrino physics in Europe to study a neutrino long baseline concept in a spirit of inclusiveness,
    to impact the priority list of High Energy Physics policy makers and of funding agencies to this new approach to the experimental discovery of leptonic CP violation.
  13 participating countries
http://euronunet.in2p3.fr/
Finished in March 2020
At the end of this COST Action 10 k€ "bonus" have been obtained to produce a short film dedicated to the project targeting scientists: https://youtu.be/PwzNzLQh-Dw

## Slide 29: ESSνSB at the European level
A H2020 EU Design Study (Call INFRADEV-01-2017)
Title of Proposal: Discovery and measurement of leptonic CP violation using an intensive neutrino Super Beam generated with the exceptionally powerful ESS linear accelerator
Duration: 4 years
Total cost: 4.7 M€
Requested budget: 3 M€
15 participating institutes from 11 European countries including CERN and ESS
6 Work Packages
Approved end of August 2017
ESSνSB
BENE (2004-2008)
ISS (2005-2007)
EUROν (2008-2012)
LAGUNA (2008-2010)
LAGUNA-LBNO (2010-2014)
COST Action CA15139 (2015-2019)

## Slide 30: Design Study ESSνSB (2018-2021)
partners: IHEP, BNL, SCK•CEN, SNS, PSI, RAL, Oslo, Hamburg
More information on:
http://essnusb.eu/
CDR end of 2021
…and after?

## Slide 31: Possible ESSνSB schedule (optimistic?) (2nd generation neutrino Super Beam)
2021: End of ESSνSB Design Study, CDR and preliminary costing
2012: inception of the project
2016-2019: beginning of COST Action EuroNuNet
2018: beginning of ESSνSB Design Study (EU-H2020)
2022-2025: Preparatory Phase, TDR
2025-2028: Preconstruction Phase, International Agreement
2028-2034: Construction of the facility and detectors, including commissioning
2035-: Data taking
Nucl. Phys. B 885 (2014) 127
2nd short film targeting general public: https://youtu.be/qAnvft0nAlg

## Slide 32: Conclusion
ESS will be soon the most powerful neutron facility for many applications.
ESS can also become a neutrino facility with enough protons to go to the 2nd oscillation maximum and increase the CPV sensitivity.
CPV: 5 σ could be reached over 60% of δCP range by ESSνSB with large physics potential.
Large associated detectors have a rich astroparticle physics program.
A preparatory phase is needed.
Rich muon program for future ESS upgrades.
COST network project CA15139 and a EU-H2020 Design Study support this project.

## Slide 33: Backup

## Slide 34: How the CPV coverage and resolution curves have been produced
T2HK:
  Same curves that Hyper-K has showed at the Neutrino Town Meeting at CERN and the one that was showed at Neutrino 2018.
  Systematics are said by T2HK to be between 3% to 4%.
  sin2 2θ13 =0.1 and θ23= π /2.
DUNE:
  Public globes file released by the DUNE collaboration with the CDR, the only change is to increase the number of years from 7 to 10.
  sin22θ13 =0.1 and θ23=π/2, to be compatible with the T2HK line.
ESSnuSB:
  Instead of considering as usual “Opt. Snowmass errors" it is only assumed an overall 3% systematic error in the different signal and background channels, more in line with T2HK assumptions.
  sin22θ13 =0.1 and θ23= π /2, to be compatible with the T2HK line.

## Slide 35: Beyond DUNE, JUNO, HyperK: ESSνSB, P2O and Neutrino factory
Roumen Tsenov
Department of Atomic Physics, University of Sofia
European Neutrino "Town" meeting and ESPP 2019 discussion, CERN, 24.10.2018

## Slide 36
ESSνSB 500 kt tank at 540 km.
ESSνSB 500 kt tank at 360 km.
ESSνSB 250 kt tank at 540 km
and 250 kt tank at 360 km.
(degrees)
CPV performance comparison between ESSnuSB, DUNE and Hyper-K
assuming 3% systematic errors for ESSnuSB in line with the other two.

## Slide 37: Fraction of δCP
Lund
Zinkgruvan
(360 km)
Garpenberg
(540 km)
2 active mines aligned…
My personal opinion:
these scenarios are too optimistic for all facilities
(E. Martinez-Fernandez)

## Slide 38: Systematic errors
Phys. Rev. D 87 (2013) 3, 033004 [arXiv:1209.5973 [hep-ph]]

## Slide 39: Comparisons
Comparison using the same systematic errors
Phys. Rev. D 87 (2013) 3, 033004 [arXiv:1209.5973 [hep-ph]]